## Slide 1: Fabric Detection System
Challenge 2 – Smart Sensor Classification
Modern Summary: Version 1 & 2

## Slide 2
Project Objective
• Build a system to detect fabric presence using sensors.
• Measure fabric properties like thickness and texture.
• Create a physical prototype using Arduino and sensors.
• Implement classification: Smooth or Wrinkled surfaces.

## Slide 3
Version 1 – Fabric Detection
• IR sensors detect light reflected by fabric.
• Ultrasonic sensor measures distance to fabric surface.
• Threshold-based logic used for fabric presence/thickness.
• Serial Monitor displays real-time sensor readings.

## Slide 4
Version 2 – Intelligent Detection
• Enhanced logic to classify surface texture.
• Collected 5 samples of both IR and Distance readings.
• Analyzed fluctuations to detect wrinkles.
• Reduced noise using averaging and range detection.

## Slide 5
Sensor Logic – Smooth vs Wrinkled
• Smooth: Stable IR and Distance readings.
• Wrinkled: High fluctuation in readings.
• IR Range > 50 OR Distance Range > 1.5 cm → Wrinkled.
• Else → Smooth.

## Slide 6
Hardware Connections
• IR Emitter: + → D7, – → GND
• IR Receiver: R → 5V, G → GND, Y → A0
• Ultrasonic Sensor: VCC → 5V, GND → GND, TRIG → D9, ECHO → D10
• All sensors on single breadboard facing fabric.

## Slide 7
Final Outcome
• Accurately detects fabric presence and texture.
• Version 2 adds classification for smooth vs wrinkled.
• Reliable and readable results using combined sensor logic.
• Well-structured prototype for real-world textile automation.